## Slide 1: Distributed Consensus and Coordination in Hardware
Birds of a feather session at Middleware’18
Hosted by: Zsolt István and Marko Vukolić

## Slide 2: Outline
Specialized hardware 101
  Programmable Switches (P4)
  Programmable NICs (ARMs)
  Programmable NICs (FPGAs)
  RDMA
Spectrum of accelerated solutions
  Examples by scope
  Examples by location
Discussion

## Slide 3: P4
Language to express forwarding rules on switches (and more)
  Flexibility: packet-forwarding policies as programs
  Expressiveness: hardware-independent packet processing algorithms using general-purpose operations and table lookups.
  Resource mapping and management: compilers manage resource allocation and scheduling.
  Software engineering: type checking, information hiding, and software reuse.
  Decoupling hardware and software evolution: architecture independent, allowing separate hardware and software upgrade cycles.
  Debugging: software models of switch architectures

## Slide 4: P4 Deployment

## Slide 5: P4 Code Example

## Slide 6: SmartNIC (Arm)
Mellanox Bluefield
  2x 25/100 Gbps NIC
  Up to 16 Arm A72 cores
  Up to 16GB Onboard DRAM
Arms can run commodity software
  Best used to implement something like OpenVSwitch
If compute-bound can’t keep up with packets!

## Slide 7: SmartNIC (FPGA)
Xilinx Alveo cards
  2x 100 Gbps NIC
  Up to 64GB Onboard DRAM
  Up to 32MB Onchip BRAM
FPGA
  Can guarantee line-rate performance by design
  Breaks traditional software tradeoffs

## Slide 8: Re-programmable Specialized Hardware
Field Programmable Gate Array (FPGA)
  Free choice of architecture
  Fine-grained pipelining, communication, distributed memory
  Tradeoff: all “code” occupies chip space
Op 1
Op 2
Op 3

## Slide 9: Programming FPGAs
Challenge: adapting algorithms to the parallelism of the FPGA
Coding: Hardware definition languages, high level languages
Synthesis: Produce a logic-gate level representation (any FPGA)
Place & route: Circuit that gets mapped onto specific FPGA
Code
Synthesized Circuit
Placed & Routed

## Slide 10: FPGA Benefits and Drawbacks
Massive parallelism – both pipeline and data-parallel execution
Arithmetic operations boosted by DSPs
Compute & Data close together thanks to BRAM
Can’t “page” code in or out
Problem is if algorithm core state doesn’t fit in BRAM
10x Less power efficient then ASICs, >10x more power efficient than CPUs

## Slide 11: RDMA

## Slide 12: Hardware summary
Programmable Switches (P4)
  Use forwarding tables
  Guarantee line-rate processing
  Very high bandwidth
  Limited state on device, limited complexity code (e.g. branches, loops)
Programmable NICs (ARMs)
  Arbitrary processing
  Can’t guarantee line-rate processing
  Lower bandwidths
Programmable NICs / Switches (FPGAs)
  Arbitrary processing*, supports complex state on device
  Can guarantee line-rate processing
  High bandwidths
RDMA NICs
  No processing, only data manipulation with low latency
  Low latency buy removing OS overhead

## Slide 13: Hardware landscape
P4 adoption by Chinese companies
  https://www.sdxcentral.com/articles/news/barefoot-scores-tofino-deals-with-alibaba-baidu-and-tencent/2017/05/
Smart NICs
  E.g., Mellanox
  Microsoft Catapult
FPGAs in the cloud
  Amazon, Baidu
RDMA support in Azure
  https://docs.microsoft.com/en-us/azure/virtual-machines/windows/sizes-hpc?toc=%2Fazure%2Fvirtual-machines%2Fwindows%2Ftoc.json

## Slide 14: Consensus in Hardware
Ordered, reliable channels
Write
Propose
Propose
Ack.
Ack.
Commit
Commit
Follower
Leader
Follower
Protocol described in: F. P. Junqueira, B. C. Reed, et al. Zab: High-performance broadcast for primary-backup systems. In DSN’11.
Tight integration with network (latency)
Low latency decision making (latency)
Pipelining (throughput)
Sequencing/reliability in network

## Slide 15: Scope of Acceleration (NICs)
Full Protocol
  DARE [1]
  FARM [2]
Common-case
  APUS [3]
Operations
  Mellanox Fabric Collective Accelerator (FCA)
[1] Poke, Marius, and Torsten Hoefler. "Dare: High-performance state machine replication on rdma networks." Proceedings of the 24th International Symposium on High-Performance Parallel and Distributed Computing. ACM, 2015.
[2] Dragojević, Aleksandar, et al. "FaRM: Fast remote memory." 11th {USENIX} Symposium on Networked Systems Design and Implementation ({NSDI} 14). 2014.
[3] Wang, Cheng, et al. "APUS: Fast and scalable Paxos on RDMA." Proceedings of the 2017 Symposium on Cloud Computing. ACM, 2017.
Remote log
KVS
Replicated operations

## Slide 16: Scope of Acceleration
Full Protocol
  Consensus in a Box [1] – FPGA
  NetChain [2] – P4 Switch
Common-case
  P4Paxos [3] (NetPaxos [4]) – P4 Switch
Operations
  SpecPaxos [5] – OpenFlow Switch
[1] István, Zsolt, et al. "Consensus in a Box: Inexpensive Coordination in Hardware." NSDI. 2016.
[2] Jin, Xin, et al. "NetChain: Scale-Free Sub-RTT Coordination." NSDI 2018
[3] Dang, Huynh Tu, et al. "Paxos made switch-y." ACM SIGCOMM Computer Communication Review 46.2 (2016): 18-24.
[4] Dang, Huynh Tu, et al. "Netpaxos: Consensus at network speed." Proceedings of the 1st ACM SIGCOMM SDN. ACM, 2015.
[5] Ports, Dan RK, et al. "Designing Distributed Systems Using Approximate Synchrony in Data Center Networks." NSDI. 2015.

## Slide 17: Consensus in a Box (Caribou)
Software clients (>10 machines simulating 1000s of clients)
  Binary protocol, but can be used as drop-in replacement for SW key-value stores (e.g. Memcached)
Client-facing and inter-node traffic: 10Gbps TCP
  <10μs consensus latency, >1M consensus rounds/s
10Gbps Ethernet
8GB DDR3 Memory
FPGA
Extension to e.g. SATA, NVMe

## Slide 18: NetChain
Implements KVS in switches
  Meta-data store, coordination
  “HalfRTT” because no need to reach an other end-host
μs replication (strong consistency)
>100Gbps bandwidth
Limitations on key/value sizes

## Slide 19: Paxos Made Switchy
Implements the Coordinator and Acceptor roles in P4 Switch
Reconfiguration and recovery, as well as management, are external
Reduces latency and cost on end-hosts

## Slide 20: Speculative Paxos

## Slide 21: Scope of Acceleration – Gains
Full Protocol
  Rely on tight integration of different layers to deliver high throughput/low latency
  Specializing the processing to the protocol
Common-case
  Benefit from cheaper processing in best case, less egress on end-host
  Detect when we are not in best case, fall back logic
  Uses less state on the devices then performing entire protocol
Operations
  Allow the end hosts to push simple “tasks” of some domain into the network
  Generate packets, gain from reducing data movement on egress link

## Slide 22: Integration of Acceleration
End hosts (DARE, FARM, Caribou)
  Easiest integration
  Most control
Split (PaxosMadeSwitchy, ERIS [1])
  Integration more complex
  Less control
Switch/Middlebox (NetChain)
  Packaged as “service”
  Independently controlled
[1] Li, Jialin, Ellis Michael, and Dan RK Ports. "Eris: Coordination-free consistent transactions using in-network concurrency control." Proceedings of the 26th Symposium on Operating Systems Principles. ACM, 2017.

## Slide 23: Coordinating control plane ops.
A special type of application – Update the changes in the SDN controller, detect errors, etc.
  Low latency operation required
  Strongly consistent view
Molero, Edgar Costa, Stefano Vissicchio, and Laurent Vanbever. "Hardware-Accelerated Network Control Planes." Proceedings of the 17th ACM Workshop on Hot Topics in Networks. ACM, 2018.
Schiff, Liron, Stefan Schmid, and Petr Kuznetsov. "In-band synchronization for distributed SDN control planes." ACM SIGCOMM Computer Communication Review 46.1 (2016): 37-43.

## Slide 24: Application scenarios
Replicated KVS
  Maintain consistent view across replicas
  Cheaper consensus  switch to strong consistency instead of eventual
  Both throughput and latency is important
  Could offload at NIC or Switch
Part of a larger application
  OLTP Database transactions – lock management
  Not necessarily KV pairs, could be a tree
  Many concurrent operations – not locking the actual data – throughput and latency both important
  Could be done as offload or as independent service
Targeting Distributed Ledgers
  Each node (many) takes part in consensus
  Operations on top can be expensive (crypto) – unclear how much it is worth optimizing the consensus layer for throughput or latency…
  In non-geo replicated scenarios coordination should become the bottleneck
  Could be done as offload or as independent service

## Slide 25: Application spectrum
1ms app time / coordination op
  Distributed ledgers (core ordering)
  Machine learning frameworks (parameter server)
100μs app time / coordination op
  Relational database engine (lock management)
  Some HPC workloads (MPI barriers)
<10μs app time / coordination op
  NoSQL database engines (distributed transactions, replication)
  Metadata stores (replication)
  SDN control plane management (update propagation)

## Slide 26: Question1: What about Geo-distribution?
Intuitively hardware acceleration is not useful in this scenario
Or: Can hardware make a difference in keeping algorithms in best case and reduce cost of reconfig/recovery?
Or: …?

## Slide 27: Question1: Geo-Distribution
World-scale
Datacenter
City-scale
Continent-sc.
Papers discussed

## Slide 28: Question2: What about BFT?
BFT involves more computation  less amenable to low level HW optimization
  Could we use hardware to keep algorithm in best case? Anything more?
  Could we use some “certification” of hardware to relax assumptions? Etc.

## Slide 29: Question3: TPUT vs. Latency?
What ranges are of interest?
What combinations are of interest?
Is the gain a linear or step function?

## Slide 30: Question3: TPUT vs Latency + Additional requirement?
>1M rounds/s
10k rounds/s
<1k rounds/s
ms
μs
Traditional Software Solutions
Most accelerated work

## Slide 31: Question4: What about programmability?
If we had an Paxos ASIC, would that be useful?
Are algorithms still changing, or we can use common building blocks?

## Slide 32: Temperature check
Do we feel that there is more to achieve in this space?
Which direction should we be looking at?

## Slide 33: 9th Workshop on Systems for Multi-core and Heterogeneous Architectures (SFMA 2019)
https://sites.google.com/site/sfma2019eurosys/
Researchers from operating systems, language runtime, virtual machine and architecture communities
Focuses on system building experiences with the new generations of parallel and heterogeneous hardware
No proceedings!
Important Dates:
  Submission: January 17, 23:55 (GMT)
  Acceptance: February 10th